## Slide 1
Lecture #4
Probabilistic Seismic Hazard Analysis
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it
https://github.com/CNardin

## Slide 2
PSHA
Probabilistic Seismic Hazard Analysis (PSHA) evaluates the exceedance (or occurrence) probability of a given ground motion intensity measure threshold at given site and time interval.
PSHA provides a framework in which uncertainties, typically include magnitude size, earthquake location, soil condition, and rate of occurrence of earthquakes, are quantified.
The calculation of seismic hazard is based on the Total Probability Theorem*
<< the probability that a fixed value of ground motionis exceeded at a given site, given the occurrence of random earthquake from the seismic source >>
*see Lecture Notes
(1)
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 3
PSHA - Steps
i. Source Characterization: probability distribution of potential earthquake locations within the source  Definition of
ii. Magnitude Characterization: temporal distribution of earthquake recurrence and size distribution
iii. Ground Motion Estimation: empirical regression models named ground motion prediction equations (GMPE)  Definition of
iv. Hazard Computation: solution of the integral (1)  probability that the ground motion parameter will be exceeded during particular time period
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 4
PSHA – Step 1: Earthquake source characterization
Goal: to identify
Fault sources: individual or multiple identified faults
Area sources: defined by polygons in which seismicity is assumed uniform
(Identification based upon the interpretation of geological, geophysical and seismological – historical data)
SOURCES
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 5
PSHA – Step 1: Earthquake source characterization
and to characterize seismic sources
Point source
Linear source
Area source
(the geometry of the source is used to identify the probability distribution of source-to-site distances)
Introduction Probabilistic Hazard Model Laboratory
DISTANCES
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 6
PSHA – Step 1: Earthquake source characterization
The geometry of the source is used to identify the probability distribution of source-to-site distances
R1: hypocentral distance
R2: epicentral distance
R3: distance to the zone of highest energy release.
R4: closest distance to the zone of rupture
R5: closest distance to the surface projection of the
fault rupture (also known as Joyner-Boore distance)
DISTANCES
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 7
PSHA – Step 1: Earthquake source characterization
Earthquakes are equally likely to occur anywhere in the area within K km of the site.
EXAMPLE
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 8
PSHA – Step 2: Earthquake size (Recurrence law)
Goal: to define distribution of
the chance of an earthquake of a given size occurring anywhere inside the source during a specified period of time
The Gutenberg-Richter law (G-R law) expresses the relationship between the magnitude and rate of cumulative number of earthquakes in any given region:
logarithm base 10 of the mean annual rate of exceedance of magnitude , overall rate of earthquakes of the source and relative ratio of small vs large magnitudes
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 9
PSHA – Step 2: Earthquake size (Recurrence law)
Bounded G-R law
Truncated exponential distribution:
• : not all the earthquakes can produce damages to the structures and a threshold on the magnitude is thus fixed. It is usually set at values from about 4.0 to 5.0.
• : magnitude scale saturates and seismic zones in question cannot generate magnitudes above this value. Estimation based on geologic evidence, geophysical data, analogies to similar tectonic regimes, or other methods.
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 10
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
given a seismic source, parameters are estimated through statistical analysis of historical data with constraints from geological evidence
paramount aspect regarding completeness and undistortion of the reference catalogue in terms of intensity/magnitude range and time intervals
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 11
PSHA – Step 3: Ground motion predictive equations (GMPE)
The most used explanatory variables are the magnitude (M), the source-to-site distance (R) and coefficients to take into account for style of faulting (F), wave propagation path, and/or local site conditions (S).
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 12
PSHA – Step 3: Ground motion predictive equations (GMPE)
Goal: estimate ground motion at the site
Identify the of interest for the situation and purposes;
Estimation of the PDF of the selected by referring to predictor variables such as the earthquake source properties
GMPEs are usually adopted to evaluate the probability that a particular exceeds a certain value, , for a given earthquake , occurring at a given distance,
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 13
PSHA – Step 3: Ground motion predictive equations (GMPE)
The most used explanatory variables are the magnitude (M), the source-to-site distance (R) and coefficients to take into account for style of faulting (F), wave propagation path, and/or local site conditions (S).
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 14
PSHA – Step 3: Ground motion predictive equations (GMPE)
Goal: Identify the 𝐼𝑀 of interest for the situation and purposes
Ground motion parameters (also called Intensity Measures, IMs) describe the most important characteristics of strong ground motion in compact and quantitative form:
• Amplitude – how large is the shaking?
• Frequency content – what frequencies are particularly prevalent in the ground motion?
• Duration – how long does the strong shaking last?
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 15
PSHA – Step 3: Ground motion predictive equations (GMPE)
Ground motion parameters
Amplitude parameters:
• Peak ground acceleration (PGA) which is the
maximum absolute value of acceleration at the
ground level;
• Peak ground velocity (PGV), the maximum
absolute value of velocity at the ground;
• Peak ground displacement (PGD) is the
maximum absolute value of displacement at the
ground
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 16
PSHA – Step 3: Ground motion predictive equations (GMPE)
Ground motion parameters
Frequency content parameters
• Response spectrum: maximum response (in
terms of displacement, velocity or acceleration,
S(𝑇, 𝜉)) of an elastic single degree- of-freedom
(SDoF) system to a particular input motion as a
function of the natural period and damping ratio.
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 17
PSHA – Step 3: Ground motion predictive equations (GMPE)
In probabilistic terms
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 18
PSHA – Step 3: Ground motion predictive equations (GMPE)
Here, for clarity, it is assumed for the mean of log peak ground acceleration (in units of g):
1. Cornell (1979)
, with of ; normally distributed
2. Campbell and Bozorgnia (1994)
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 19
PSHA – Step 4: Hazard Computation
The seismic hazard curve is a function representing the annual frequency of exceeding various levels of ground shaking (i.e. the ) at a specific site. The curve is obtained by integration of the previously three steps over all possible magnitudes and earthquakes locations.
Seismic hazard curves are obtained for individual sources and, then, combined to express the aggregate hazard at a particular site.
Then:
(2)
Introduction Probabilistic Hazard Model Laboratory
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 20
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Introduction Probabilistic Hazard Model Laboratory
References
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it

## Slide 21
Trento, 03 February 2023
Chiara Nardin, Ph.D.
chiara.nardin@unitn.it