## Slide 1
Fragility Analysis
Formulation and MatLab Computation
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
https://github.com/CNardin/Lecture/tree/2021/ISPS

## Slide 2
Fragility curves for different damage limit states or thresholds.
Fragility Analysis
VULNERABILITY
Vulnerability analysis
engineering demand par.
VULNERABILITY
Damage analysis
damage measure
Fragility Analysis | MatLab | References

## Slide 3
Goal: to perform fragility analysis
Given the provided set of ground motions, perform a classical and truncated incremental dynamic analysis (IDA) and determine fragility curves for:
ATTEL – moment resistant frame (MRF);
ATTEL – braced frame (BF)
by considering both
Linear elastic behaviour
Bouc – Wen model for hysteresis
3D model of the case study ATTEL – SERA project.
Fragility Analysis | MatLab | References

## Slide 4
Main steps:
Definition of the numerical model
Input and IM selection
Definition of damage limit states and reference EDP
Performing non-linear time histories analysis (IDA, truncated IDA, cloud, MSA …)
Collecting results pairs and computing fragility
3D model of the case study ATTEL – SERA project.
Fragility Analysis | MatLab | References

## Slide 5
T1 = 2.79 s
T1 = 0.46 s
[1]BURSI, PUCINOTTI, TONDINI, ZANON, Tests and model calibration of high strength steel tubular beam-to-column and column-base composite joints for moment-resisting structures, Earthquake Engineering and Structural Dynamics, (2015).
3D model of the case study ATTEL – SERA project.
Step 1: the case study ATTEL(1)
Main sections of the moment resistent frame and the braced one.
Fragility Analysis | MatLab | References

## Slide 6
Designed according to EC8 and modelled in OS:
beam and column elements with linear elastic behavior
mechanical nonlinearities
geometric nonlinearities
Model of the structure in OpenSees.
Fragility Analysis | MatLab | References
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 7
to reduce computational burden
to reduce required simulation times
high fidelity model in OpenSees - OS
simplified model MDOF in MATLAB ® - ML
High number of analysis
for seismic simulations
Calibration oriented to correspondence of:
main periods
modes of vibrating
dissipative behavior
Fragility Analysis | MatLab | References

## Slide 8
Trento, 02 December 2020
Ph.D. Student: Chiara Nardin
chiara.nardin@unitn.it
Hysteretic model of Bouc Wen.
Formulation of the problem and examples of hysteretic cycles.
Hysteretic model of Bouc Wen
Fragility Analysis | MatLab | References

## Slide 9
Step 2: input and IM selection
main features
Dataset NGA-WEST 2
crustal earthquakes
Mw > 6
Rrup > 10 km
Vs30 > 600 m/s
206 ground motions
fault mechanism
reverse REV
strike slip SS
PGA [g]
PGV [cm/s]
PGD [cm]
IMs investigated
Sa (T1) [g rad2]
Sv (T1) [cm rad/s]
Sd (T1) [cm]
PSa (T1) [g rad2]
PSv (T1) [cm rad/s]
Fragility Analysis | MatLab | References

## Slide 10
Step 2: input and IM selection
Acceleration, velocity and displacement response spectra with mean value, 10-th and 90-th quantile.
Scatter plot for correlation.
Data exploration of recorded gms
Scatter plot and statistic tools to evaluate proper IM
Fragility Analysis | MatLab | References

## Slide 11
Step 2: input and IM selection
Codes:
%% Ground motions
Ground_motions = load('accelrot_cellarray.mat');
%
NN = [1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 16, 17, 19, 21, 23, 24,...
25, 26, 28, 29, 30, 31, 32, 33, 34, 36, 37]; % number ID of the SS ground motions
DT = [0.01 , 0.01 , 0.005, 0.005, 0.005, 0.005, 0.02 , 0.02, 0.02, 0.01,...
0.01 , 0.01 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02, 0.01, 0.01,...
0.005, 0.005, 0.005, 0.005, 0.02 , 0.005, 0.005, 0.01, 0.01, 0.01,...
0.01 , 0.005, 0.005, 0.02 , 0.005, 0.01 , 0.01]; % integration time step
Fragility Analysis | MatLab | References
https://github.com/CNardin/Lecture/tree/2021/ISPS

## Slide 12
Step 3: Definition of damage limit states and reference EDP
Document FEMA 356 - Prestandard and Commentary for the Seismic Rehabilitation of Buildings; Table C1-3 - Structural Performance Levels and Damage.
MRF
BF
Fragility Analysis | MatLab | References

## Slide 13
Step 3: Definition of damage limit states and reference EDP
Codes:
%% MDOF Properties
% Choose between the structural system
MDOF_properties_BW_MRF
MDOF_properties_BW_BF
% and between linear or hysteretic behaviour
%% Structural behaviour
System_type = ‘le’; % ‘bw’
% bw = bouc-wen
% le = linear elastic
…
%% Limit States
LS = [0.50 0.75 1 2 3]*4/100;
for ls_i = 1:numel(LS)
ls_val = LS(ls_i)
Main_IDA_o_t
ls_i = ls_i + 1;
end
Fragility Analysis | MatLab | References

## Slide 14
Step 4: Performing non-linear time histories analysis
Codes:
%% Initial condition
Mat.dFe=zeros(Mat.NDOF,numel(a_g_norm)); % Preallocation for the load for the time series
a_g = a_g_norm*scale; % Scaled ground motion
Mat.Fe=Mat.M*Mat.r'*a_g'*g;
%% Computation response
[HistVarBw]=ResponceMDF_Bw(Mat);
edp = max(abs(HistVarBw.eps(1,:)));
EDP(i) = edp; %store the EDP for each time history analysis
SCALE(i) = scale; %store the scale factor for each time history analysis…
Fragility Analysis | MatLab | References

## Slide 15
Step 5: Computing fragilities
Codes:
%% Untruncated IDA
[parmhat,parmci] = lognfit(IM_t_c ,0.01);
mu_IDA = parmhat(1);
sigma_IDA = parmhat(2);
%% Truncated IDA
IM_max = 2.2;
IM_trunc = IM_t_c(IM_t_c < IM_max); % take only the results with IM < IM_max
eq_over = sum(IM_t_c >= IM_max); % number of analyses reached IM_max without collapsing
% Maximum likelihood fit, using equation (1) and (2) of previously slides
[mu_IDA_t, sigma_IDA_t ] = truncated_ida(IM_trunc, IM_max, eq_over);
Fragility Analysis | MatLab | References

## Slide 16
Step 5: Computing fragilities - Results
Fragility Analysis | MatLab | References

## Slide 17
Step 5: Computing fragilities - Results
Fragility Analysis | MatLab | References

## Slide 18
References:
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Stucchi M., Meletti C., Montaldo V., Akinci A., Faccioli E., Gasperini P., Malagnini L., Valensise G. (2004). Pericolosità sismica di riferimento per il territorio nazionale MPS04. Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/sh/mps04/agKramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
http://zonesismiche.mi.ingv.it/  Italian database
Fragility Analysis | MatLab | References

## Slide 19
References:
Mackie, K & Stojadinovic, Bozidar. (2003). Seismic Demands for Performance-Based Design of Bridges.
Bursi, Pucinotti, Tondini, Zanon, Tests and model calibration of high strength steel tubular beam-to-column and column-base composite joints for moment-resisting structures, Earthquake Engineering and Structural Dynamics, (2015).
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Charalampakis, A. & Koumousis,V. (2010). Parameters of Bouc–Wen Model Revisited, Applied Mechanics.
Haukaas, T. & Der Kiureghian, A. (2004). Finite Element Reliability and Sensitivity Methods for Performance-Based Earthquake Engineering, tech. rep., PEER - Pacific Earthquake Engineering Research Center.
Fragility Analysis | MatLab | References

## Slide 20
Thanks for the attention!
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
https://github.com/CNardin