## Slide 1
Lecture #4
Fragility analysis
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
https://github.com/CNardin/Lecture/tree/2021/ISPS

## Slide 2
Fragility Analysis
Fragility (or Vulnerability) Analysis is the second step of the PBEE-PEER framework
Useful definitions:
seismic fragility function := the conditional probability of an event (e.g. a defined limit/damage state) given the observation of an intensity measure which describe the seismic event.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Hazard analysis
intensity measure
Loss analysis
decision variable
HAZARD
VULNERABILITY
Damage analysis
damage measure
DECISION MAKING
VULNERABILITY
Vulnerability analysis
engineering demand par.
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 3
The fragility curve is defined as the conditional probability of failure of a structure, or its critical components, at given values of seismic intensity measures (IMs).
In practice, a fragility curve is calculated as the conditional probability that the damage measure (D) exceeds a critical threshold, for a given seismic IM.
Fragility Analysis
VULNERABILITY
Vulnerability analysis
engineering demand par.
VULNERABILITY
Damage analysis
damage measure
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 4
INTENSITY MEASURE | DAMAGE STATE
in terms of: Efficiency, i.e. variability of an EDP for a given IM; Robustness, i.e. efficiency between IM-EDP at different period ranges; Practicality, i.e. correlation to known and easy identifiable engineering quantities; Sufficiency, i.e. validity of EDP¦IM as statistically independent from gm site characteristics; Effectiveness, i.e. ability to evaluate an analytical relation. | Should suit the specific structural problem  associate each damage state to a specific EDP Categorical variables, i.e. no damages – minor – ; Probabilistic or deterministic relationship between EDP and D
in terms of: Efficiency, i.e. variability of an EDP for a given IM; Robustness, i.e. efficiency between IM-EDP at different period ranges; Practicality, i.e. correlation to known and easy identifiable engineering quantities; Sufficiency, i.e. validity of EDP¦IM as statistically independent from gm site characteristics; Effectiveness, i.e. ability to evaluate an analytical relation. | 
Fragility Analysis: key aspects
VULNERABILITY
Vulnerability analysis
engineering demand par.
VULNERABILITY
Damage analysis
damage measure
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 5
EMPIRICAL | ANALYTICAL | EXPERT OPINION | HYBRID
by fitting a function to observational data from past earthquakes or lab tests collections pairs of level of excitation and categorical variables of damage or collapse | by defining analytical structural model and analyzing its performance under different levels of the seismic hazard static, i.e. hazard as response spectrum and push-over analysis vs dynamic, i.e. collection of gms and simulations on FEM via NLA | by polling one or more experts of the given structural asset to guess or estimate the failure probability for a given hazard level | based on combination of the different methods
Class of fragilities
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 6
Analytical fragility functions: steps
Definition of a numerical model:
Selection of a suitable given the structure
Selection of a suitable set of gms for the location
Selection of an of interest
Definition of damage limit states via thresholds
Scale each gm based on the given eventually until collapse
Save each threshold- pair for each gm
Full IDA
Truncated IDA
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 7
Computation of fragility function
FULL IDA | TRUNCATED IDA
damage state results, since reached the given damage state where is the CDF of the normal distribution and | upper limit; data that causes collapse , data that do not cause collapse a) b)
FULL IDA | TRUNCATED IDA
Hp: - assume a lognormal probability distribution for the random variable associated with given
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 8
Computation of fragility function
TRUNCATED IDA
TRUNCATED IDA
The likelihood for the entire set of data
And the log likelihood
Estimation of parameters by optimization
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 9
Lecture #4
Fragility Analysis – MatLab Tutorial
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
https://github.com/CNardin/ISPS.git

## Slide 10
Goal: to perform fragility analysis
Given the provided set of ground motions, perform a classical and truncated incremental dynamic analysis (IDA) and determine fragility curves for:
ATTEL – moment resistant frame (MRF);
ATTEL – braced frame (BF)
by considering both
Linear elastic behaviour
Bouc – Wen model for hysteresis
3D model of the case study ATTEL – SERA project.
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 11
Main steps:
Definition of the numerical model
Input and IM selection
Definition of damage limit states and reference EDP
Performing non-linear time histories analysis (IDA, truncated IDA, cloud, MSA …)
Collecting results pairs and computing fragility
3D model of the case study ATTEL – SERA project.
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 12
T1 = 2.79 s
T1 = 0.46 s
[1]BURSI, PUCINOTTI, TONDINI, ZANON, Tests and model calibration of high strength steel tubular beam-to-column and column-base composite joints for moment-resisting structures, Earthquake Engineering and Structural Dynamics, (2015).
3D model of the case study ATTEL – SERA project.
Step 1: the case study ATTEL(1)
Main sections of the moment resistent frame and the braced one.
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 13
Designed according to EC8 and modelled in OS:
beam and column elements with linear elastic behavior
mechanical nonlinearities
geometric nonlinearities
Model of the structure in OpenSees.
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 14
to reduce computational burden
to reduce required simulation times
high fidelity model in OpenSees - OS
simplified model MDOF in MATLAB ® - ML
High number of analysis
for seismic simulations
Calibration oriented to correspondence of:
main periods
modes of vibrating
dissipative behavior
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 15
Hysteretic model of Bouc Wen.
Formulation of the problem and examples of hysteretic cycles.
Hysteretic model of Bouc Wen
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 16
Step 2: input and IM selection
main features
Dataset NGA-WEST 2
crustal earthquakes
Mw > 6
Rrup > 10 km
Vs30 > 600 m/s
206 ground motions
fault mechanism
reverse REV
strike slip SS
PGA [g]
PGV [cm/s]
PGD [cm]
IMs investigated
Sa (T1) [g rad2]
Sv (T1) [cm rad/s]
Sd (T1) [cm]
PSa (T1) [g rad2]
PSv (T1) [cm rad/s]
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 17
Step 2: input and IM selection
Acceleration, velocity and displacement response spectra with mean value, 10-th and 90-th quantile.
Scatter plot for correlation.
Data exploration of recorded gms
Scatter plot and statistic tools to evaluate proper IM
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 18
Step 2: input and IM selection
Codes:
%% Ground motions
Ground_motions = load('accelrot_cellarray.mat');
%
NN = [1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 16, 17, 19, 21, 23, 24,...
25, 26, 28, 29, 30, 31, 32, 33, 34, 36, 37]; % number ID of the SS ground motions
DT = [0.01 , 0.01 , 0.005, 0.005, 0.005, 0.005, 0.02 , 0.02, 0.02, 0.01,...
0.01 , 0.01 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02 , 0.02, 0.01, 0.01,...
0.005, 0.005, 0.005, 0.005, 0.02 , 0.005, 0.005, 0.01, 0.01, 0.01,...
0.01 , 0.005, 0.005, 0.02 , 0.005, 0.01 , 0.01]; % integration time step
Fragility Analysis | MatLab | References
https://github.com/CNardin/Lecture/tree/2021/ISPS
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 19
Step 3: Definition of damage limit states and reference EDP
Document FEMA 356 - Prestandard and Commentary for the Seismic Rehabilitation of Buildings; Table C1-3 - Structural Performance Levels and Damage.
MRF
BF
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 20
Step 3: Definition of damage limit states and reference EDP
Codes:
%% MDOF Properties
% Choose between the structural system
MDOF_properties_BW_MRF
MDOF_properties_BW_BF
% and between linear or hysteretic behaviour
%% Structural behaviour
System_type = ‘le’; % ‘bw’
% bw = bouc-wen
% le = linear elastic
…
%% Limit States
LS = [0.50 0.75 1 2 3]*4/100;
for ls_i = 1:numel(LS)
ls_val = LS(ls_i)
Main_IDA_o_t
ls_i = ls_i + 1;
end
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 21
Step 4: Performing non-linear time histories analysis
Codes:
%% Initial condition
Mat.dFe=zeros(Mat.NDOF,numel(a_g_norm)); % Preallocation for the load for the time series
a_g = a_g_norm*scale; % Scaled ground motion
Mat.Fe=Mat.M*Mat.r'*a_g'*g;
%% Computation response
[HistVarBw]=ResponceMDF_Bw(Mat);
edp = max(abs(HistVarBw.eps(1,:)));
EDP(i) = edp; %store the EDP for each time history analysis
SCALE(i) = scale; %store the scale factor for each time history analysis…
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 22
Step 5: Computing fragilities
Codes:
%% Untruncated IDA
[parmhat,parmci] = lognfit(IM_t_c ,0.01);
mu_IDA = parmhat(1);
sigma_IDA = parmhat(2);
%% Truncated IDA
IM_max = 2.2;
IM_trunc = IM_t_c(IM_t_c < IM_max); % take only the results with IM < IM_max
eq_over = sum(IM_t_c >= IM_max); % number of analyses reached IM_max without collapsing
% Maximum likelihood fit, using equation (1) and (2) of previously slides
[mu_IDA_t, sigma_IDA_t ] = truncated_ida(IM_trunc, IM_max, eq_over);
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 23
Step 5: Computing fragilities - Results
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 24
Step 5: Computing fragilities - Results
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 25
References:
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Stucchi M., Meletti C., Montaldo V., Akinci A., Faccioli E., Gasperini P., Malagnini L., Valensise G. (2004). Pericolosità sismica di riferimento per il territorio nazionale MPS04. Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/sh/mps04/agKramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
http://zonesismiche.mi.ingv.it/  Italian database
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 26
References:
Mackie, K & Stojadinovic, Bozidar. (2003). Seismic Demands for Performance-Based Design of Bridges.
Bursi, Pucinotti, Tondini, Zanon, Tests and model calibration of high strength steel tubular beam-to-column and column-base composite joints for moment-resisting structures, Earthquake Engineering and Structural Dynamics, (2015).
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Charalampakis, A. & Koumousis,V. (2010). Parameters of Bouc–Wen Model Revisited, Applied Mechanics.
Haukaas, T. & Der Kiureghian, A. (2004). Finite Element Reliability and Sensitivity Methods for Performance-Based Earthquake Engineering, tech. rep., PEER - Pacific Earthquake Engineering Research Center.
Fragility Analysis | MatLab | References
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it

## Slide 27
Thanks for the attention!
Chiara Nardin – Ph.D., M.Sc., Eng. in Civil Engineering
https://github.com/CNardin
Trento, 03 February 2023
Ph.D. Chiara Nardin
chiara.nardin@unitn.it