## Slide 1
Ingegneria Sismica e Progettazione Strutturale
Probabilistic Seismic Hazard Analysis
Prof. Marco Broccardo – Ph.D., M.Sc., Eng. in Civil Engineering
Ph.D. Student Chiara Nardin – M.Sc., Eng. in Civil Engineering

## Slide 2
PSHA
Probabilistic Seismic Hazard Analysis (PSHA) evaluates the exceedance (or occurrence) probability of a given ground motion intensity measure threshold at given site and time interval.
PSHA provides a framework in which uncertainties, typically include magnitude size, earthquake location, soil condition, and rate of occurrence of earthquakes, are quantified.
The calculation of seismic hazard is based on the Total Probability Theorem*
<< the probability that a fixed value of ground motionis exceeded at a given site, given the occurrence of random earthquake from the seismic source >>
Introduction Probabilistic Hazard Model Laboratory
*see Lecture Notes
(1)

## Slide 3
PSHA - Steps
i. Source Characterization: probability distribution of potential earthquake locations within the source  Definition of
ii. Magnitude Characterization: temporal distribution of earthquake recurrence and size distribution
iii. Ground Motion Estimation: empirical regression models named ground motion prediction equations (GMPE)  Definition of
iv. Hazard Computation: solution of the integral (1)  probability that the ground motion parameter will be exceeded during particular time period
Introduction Probabilistic Hazard Model Laboratory

## Slide 4
PSHA – Step 1: Earthquake source characterization
Goal: to identify
Fault sources: individual or multiple identified faults
Area sources: defined by polygons in which seismicity is assumed uniform
(Identification based upon the interpretation of geological, geophysical and seismological – historical data)
Introduction Probabilistic Hazard Model Laboratory
SOURCES

## Slide 5
PSHA – Step 1: Earthquake source characterization
and to characterize seismic sources
Point source
Linear source
Area source
(the geometry of the source is used to identify the probability distribution of source-to-site distances)
Introduction Probabilistic Hazard Model Laboratory
DISTANCES

## Slide 6
PSHA – Step 1: Earthquake source characterization
The geometry of the source is used to identify the probability distribution of source-to-site distances
R1: hypocentral distance
R2: epicentral distance
R3: distance to the zone of highest energy release.
R4: closest distance to the zone of rupture
R5: closest distance to the surface projection of the
fault rupture (also known as Joyner-Boore distance)
Introduction Probabilistic Hazard Model Laboratory
DISTANCES

## Slide 7
PSHA – Step 1: Earthquake source characterization
Earthquakes are equally likely to occur anywhere in the area within K km of the site.
Introduction Probabilistic Hazard Model Laboratory
EXAMPLE

## Slide 8
PSHA – Step 2: Earthquake size (Recurrence law)
Goal: to define distribution of
the chance of an earthquake of a given size occurring anywhere inside the source during a specified period of time
The Gutenberg-Richter law (G-R law) expresses the relationship between the magnitude and rate of cumulative number of earthquakes in any given region:
logarithm base 10 of the mean annual rate of exceedance of magnitude , overall rate of earthquakes of the source and relative ratio of small vs large magnitudes
Introduction Probabilistic Hazard Model Laboratory

## Slide 9
PSHA – Step 2: Earthquake size (Recurrence law)
Bounded G-R law
Truncated exponential distribution:
• : not all the earthquakes can produce damages to the structures and a threshold on the magnitude is thus fixed. It is usually set at values from about 4.0 to 5.0.
• : magnitude scale saturates and seismic zones in question cannot generate magnitudes above this value. Estimation based on geologic evidence, geophysical data, analogies to similar tectonic regimes, or other methods.
Introduction Probabilistic Hazard Model Laboratory

## Slide 10
PSHA – Step 2: Earthquake size (Recurrence law)
Observations:
given a seismic source, parameters are estimated through statistical analysis of historical data with constraints from geological evidence
paramount aspect regarding completeness and undistortion of the reference catalogue in terms of intensity/magnitude range and time intervals
Introduction Probabilistic Hazard Model Laboratory

## Slide 11
PSHA – Step 3: Ground motion predictive equations (GMPE)
Goal: estimate ground motion at the site
Identify the of interest for the situation and purposes;
Estimation of the PDF of the selected by referring to predictor variables such as the earthquake source properties
GMPEs are usually adopted to evaluate the probability that a particular exceeds a certain value, , for a given earthquake , occurring at a given distance,
Introduction Probabilistic Hazard Model Laboratory

## Slide 12
PSHA – Step 3: Ground motion predictive equations (GMPE)
Ground motion parameters
Ground motion parameters (also called Intensity Measures, IMs) describe the most important characteristics of strong ground motion in compact and quantitative form:
• Amplitude – how large is the shaking?
• Frequency content – what frequencies are particularly prevalent in the ground motion?
• Duration – how long does the strong shaking last?
Introduction Probabilistic Hazard Model Laboratory

## Slide 13
PSHA – Step 3: Ground motion predictive equations (GMPE)
Ground motion parameters
Amplitude parameters:
• Peak ground acceleration (PGA) which is the
maximum absolute value of acceleration at the
ground level;
• Peak ground velocity (PGV), the maximum
absolute value of velocity at the ground;
• Peak ground displacement (PGD) is the
maximum absolute value of displacement at the
ground
Introduction Probabilistic Hazard Model Laboratory

## Slide 14
PSHA – Step 3: Ground motion predictive equations (GMPE)
Ground motion parameters
Frequency content parameters
• Response spectrum: maximum response (in
terms of displacement, velocity or acceleration,
S(𝑇, 𝜉)) of an elastic single degree- of-freedom
(SDoF) system to a particular input motion as a
function of the natural period and damping ratio.
Introduction Probabilistic Hazard Model Laboratory

## Slide 15
PSHA – Step 3: Ground motion predictive equations (GMPE)
In probabilistic terms
Introduction Probabilistic Hazard Model Laboratory

## Slide 16
PSHA – Step 3: Ground motion predictive equations (GMPE)
The most used explanatory variables are the magnitude (M), the source-to-site distance (R) and coefficients to take into account for style of faulting (F), wave propagation path, and/or local site conditions (S).
Introduction Probabilistic Hazard Model Laboratory

## Slide 17
PSHA – Step 3: Ground motion predictive equations (GMPE)
Here, for clarity, it is assumed for the mean of log peak ground acceleration (in units of g):
1. Cornell (1979)
, with of ; normally distributed
2. Campbell and Bozorgnia (1994)
Introduction Probabilistic Hazard Model Laboratory

## Slide 18
PSHA – Step 4: Hazard Computation
The seismic hazard curve is a function representing the annual frequency of exceeding various levels of ground shaking (i.e. the ) at a specific site. The curve is obtained by integration of the previously three steps over all possible magnitudes and earthquakes locations.
Seismic hazard curves are obtained for individual sources and, then, combined to express the aggregate hazard at a particular site.
Then:
Introduction Probabilistic Hazard Model Laboratory
(2)

## Slide 19
References
Baker J. W. (2008). An Introduction to Probabilistic Seismic Hazard Analysis (PSHA), White Paper, Version 1.3, 72 pp.
Kramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
Wells, D.L. and Coppersmith, K.J. (1994) New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement. Bull. Seism. Soc. Am., 84, 974-1002.
Cornell, C.A. (1968). Engineering seismic risk analysis, Bull. Seism. Soc. Am., 58, 1583-1606.
Broccardo, M. (2018) Probabilistic seismic risk analysis for civil systems, Lecture Notes
Introduction Probabilistic Hazard Model Laboratory

## Slide 20
Ingegneria Sismica e Progettazione Strutturale
PSHA – Assignment 1
Ph.D. Candidate Chiara Nardin – M.Sc., Eng. in Civil Engineering
https://github.com/kia13nn/ISPS.git

## Slide 21
Goal: to perform a PSHA analysis
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
Introduction Probabilistic Hazard Model Laboratory
http://esse1-gis.mi.ingv.it/
Seismic hazard map: shaking parameter PGA, site Palmoli (CH) Latitude 41,527 – Longitude 14,483.

## Slide 22
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
Different characteristics of zonation by:
Seismogenetic faults and mechanisms (direct, inverse, strike-slip …)
Hypocenter depth (shallow, intermediate, deep)
ect.
Introduction Probabilistic Hazard Model Laboratory
Italian database and catalogue of the overall seismicity
http://zonesismiche.mi.ingv.it/

## Slide 23
Step 1: Source characterization
Localize seismogenetic zones: Italian ZS9* model for application of the attenuation law
Introduction Probabilistic Hazard Model Laboratory
http://zonesismiche.mi.ingv.it/

## Slide 24
Step 1: Source characterization
Extrapolate information regarding the source and its bound limits: convert coordinates from deg2utm for each sources
Introduction Probabilistic Hazard Model Laboratory
 | Coordinates |  |  |  | 
 | WGS 84 |  | UTM |  | UTM-Z
Location | long (x) | lat (y) |  |  | 
Palmoli | 14,48 | 41,63 | 465.293 | 4643124 | 33 T
Source | b | Mw Max | Mw Min | Rate
S1 | -1,11 | 6,37 | 4,76 | 0,21
S2 | -1,09 | 7,06 | 4,76 | 0,14
… | … | … | … | …
ZS9-918 | S1 |  |  |  |  | 
WGS 84 |  | UTM |  | UTM-Z | UTM-INPORT | 
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907
12,27012 | 44,10645 | 281523,5 | 4887320 | 33 T | -183.769 | 244.196
13,54116 | 43,2943 | 381660,3 | 4794530 | 33 T | -83.633 | 151.405
14,181 | 42,47483 | 432678,9 | 4702824 | 33 T | -32.614 | 59.699
14,37249 | 42,14993 | 448153,3 | 4666614 | 33 T | -17.140 | 23.489
14,27923 | 41,85719 | 440174,4 | 4634171 | 33 T | -25.118 | -8.953
13,1518 | 43,02822 | 349423 | 4765606 | 33 T | -115.870 | 122.481
12,11651 | 43,79397 | 268015,9 | 4853032 | 33 T | -197.277 | 209.907

## Slide 25
Step 1: Source characterization - Location
Define the distribution of
To simplify, consider 1 source with a regular zonation of .
So, the distribution of an epicenter being located at a distance of less than r is:
Introduction Probabilistic Hazard Model Laboratory
CDF:
PDF:

## Slide 26
Step 1: Source characterization
Codes:
Read source.xls file
Run section Earthquake source characterization in the attached Matlab code or load variable seismic_source.mat already prepared with the previously seen data
Introduction Probabilistic Hazard Model Laboratory

## Slide 27
Step 1: Source characterization - Location
Codes:
% PDF of R
rmax = Rmax*100; % 50km
rmin = Rmin.*100; % site
r_step = R_step;
r = rmin:r_step:(rmax-r_step);
Fr = r.^2./rmax.^2;
fr = 2*r./rmax.^2;
DFr = r_step;
frdiscr = zeros(1,numel(Fr));
Frdiscr = zeros(1,numel(Fr));
for idr = 2:numel(Fr)
frdiscr(idr) = -(Fr(idr-1)-Fr(idr))./(DFr);
Frdiscr(idr) = Frdiscr(idr-1)+Fr(idr);
end
Introduction Probabilistic Hazard Model Laboratory

## Slide 28
Step 2: Earthquake size
Define the distribution of
Gutenberg-Richter bounded defines the relationship between the magnitude and rate of cumulative number of earthquakes
Introduction Probabilistic Hazard Model Laboratory
)
CDF:
PDF:

## Slide 29
Step 2: Earthquake size
Define the distribution of : Discretize
Converting the continuous distribution of magnitudes into a discrete set of magnitudes holds
where are the discrete set of magnitudes ordered so that
Introduction Probabilistic Hazard Model Laboratory
Codes:
% PDF of M
Nm = 1000; % No. of discretized points between m0 and mu for numerical integration
M = linspace(m0,mu,Nm); %mo = m_min
fM = beta*exp(-beta*(M-m0))/(1-exp(-beta*(mu-m0)));
dM=M(2)-M(1);
Mdiscr=fM*dM;

## Slide 30
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
These models predict the probability distribution of ground motion intensity, as a function of many predictor variables such as the earthquake’s magnitude, distance, faulting mechanism, the near-surface site conditions, etc.
To describe this probability distribution, prediction models take the following general form:
where
is the natural log of the ground motion intensity measure of interest;
is modeled as a random variable and is represented by a normal distribution;
and are the predicted mean and standard deviation of ;
and are functions of the earthquake’s magnitude , distance and other parameters

## Slide 31
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
Here, for clarity, it is assumed Cornell (1979) for the mean of log peak ground acceleration (in units of g):
with
of ;
normally distributed

## Slide 32
Step 3: Ground motion estimation
Introduction Probabilistic Hazard Model Laboratory
Define effects : Attenuation models or prediction models
We can thereby compute the probability of exceeding any PGA level using knowledge of this mean and standard deviation:
where is the standard normal cumulative distribution function.
N.B.: these probabilities correspond to the fraction
of the corresponding PDFs that are shaded.

## Slide 33
Step 3: Ground motion estimation
Define effects : Attenuation models or prediction models
Introduction Probabilistic Hazard Model Laboratory
Codes:
function [mean_im, sigma_im] = GMPE(magnitude,R_distance)
%Cornell et al. (1979): Ground motion predictive equation for PGA
mean_lnPGA = -0.152+0.859*magnitude -1.803*log(R_distance+25);
mean_PGA = exp(mean_lnPGA);
mean_im = mean_PGA;
sigma_im = 0.57;
end

## Slide 34
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute
Compute the probability of exceeding an IM intensity level x, given occurrence of a future earthquake from a single source:
II. Compute the rate of IM > x for each single source:

## Slide 35
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute
III. Considering all sources by the sum of the rates of IM > x from each individual source, we can write:
where is the number of sources considered, and denote the magnitude ~ distance
distributions for source i
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 36
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Combine all information: compute - Discretize
IV. By discretizing:
where the range of possible and have been discretized into and intervals, respectively
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 37
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Goal and results
Through the scheme depicted in (1), compute:
the annual hazard curve for each fault;
the 50 years hazard curve for each fault;
the 475 years hazard curve for each fault
for the highlighted seismic site.
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 38
Step 4: Hazard Computation
Introduction Probabilistic Hazard Model Laboratory
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 39
Summary
Introduction Probabilistic Hazard Model Laboratory
Location
Poisson model
𝑃=1−𝑒^(−𝜆𝑡) Poisson model
Size
Time
source site distance
𝑓_𝑅 (𝑟) source site distance
GMPE
magnitude distribution
𝑓_𝑀 (𝑚) magnitude distribution
attenuation law
𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟) attenuation law
Location
Size
Time
GMPE
Notes: λ(𝑀>𝑚_𝑚𝑖𝑛)∫_(𝑟_𝑚𝑖𝑛)^(𝑟_𝑚𝑎𝑥)▒∫_(𝑚_𝑚𝑖𝑛)^(𝑚_𝑚𝑎𝑥)▒〖𝑃(𝐼𝑀>𝑖𝑚 ┤|𝑀=𝑚 , 𝑅=𝑟)〗 𝑓_𝑅^((𝑛) ) (𝑟) 𝑓_𝑀^((𝑛) ) (𝑚)𝑑𝑟𝑑𝑚

## Slide 40
References
Stucchi M., Meletti C., Montaldo V., Akinci A., Faccioli E., Gasperini P., Malagnini L., Valensise G. (2004). Pericolosità sismica di riferimento per il territorio nazionale MPS04. Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/sh/mps04/agKramer, S.L. (1996) Geotechnical earthquake engineering. Prentice Hall, Upper Saddle River, N.J.
http://zonesismiche.mi.ingv.it/  Italian database
Introduction Probabilistic Hazard Model Laboratory